## Slide 1
USGS RESPONSE TO FLOODS
FLASH FLOODS of AUGUST 10, 2009
Gowanda and Silver Creek, NY
Cattaraugus Creek
New York State Thruway
Notes: Cattaraugus Creek at NYS thruway

## Slide 2
Ensure uninterrupted stage-data collection at USGS gaging stations

## Slide 3
Measure streamflow

## Slide 5
FLASH FLOODS of AUGUST 10, 2009
Gowanda and Silver Creek, NY
NY Routes 5 & 20
Notes: Intersection of Thruway access road and Routes 5 & 20 at Irving, NY

## Slide 6
Composite reflectivity image taken at 8:27 PM EDT, August 9 (National Weather Service)

## Slide 7
Composite reflectivity image taken at 9:36 PM EDT, August 9 (National Weather Service)

## Slide 8
Storm-total radar derived precipitation (NWS)
Max. Recorded Precipitation
5.98 inches in 1.5 hr
Notes: The two storm systems intersected approximately along the Chautauqua-Cattaraugus-Erie Counties borders.
Producing torrential rainfall – up to almost 6 inches in 1.5 hours – between 1030 PM and midnight.

## Slide 9
Storm Recurrence Interval
Maximum Daily Total Precipitation
7.27 inches 200 to 500 yr RI
Maximum Storm Total
5.98 inches in 90 min > 500 yr RI

## Slide 12
Silver Creek Trailer Park (photo by NWS)

## Slide 16
The tri-county area declared a Federal disaster area
More than $45 million in Federal disaster assistance
to more than 1,500 individuals and
an estimated 1,100 public projects
Combined total estimate of damages
was greater than $90 million

## Slide 17
Notes: USGS continuous-record gages and
Peak-flow monitoring sites

## Slide 18
Gage Height and Streamflow
Cattaraugus Creek at Gowanda
Chart: GAGE HEIGHT, IN FEET ABOVE GAGE DATUM
Notes: USGS basic data output

## Slide 19
Notes: Slope-area
Flow-through- culvert
Contracted opening
Critical depth method
Flow-over-road

## Slide 23
Gowanda
Notes: 243 highwater marks were surveyed

## Slide 24
Silver
Creek

## Slide 25
Notes: 2009 elevations along Thatcher and Grannis were, at some locations, 2 to 4 ft higher than FEMA elevations

## Slide 27
Cattaraugus Creek at Gowanda
Slope-Area Computation: 33,200 cubic feet per second

## Slide 28
Thatcher Brook at Gowanda
Slope-Area Computation: 7,600 cubic feet per second
Notes: 1986 flood was about 4-5 ft lower; computed Q was 3,100 cfs

## Slide 29
Silver Creek
Walnut Creek
Jackson St. underpass

## Slide 30
Silver Creek (below confluence with Walnut Creek)
Contracted-Opening Computation:
19,000 cubic feet per second

## Slide 31
Silver Creek – Flow thru railroad underpass
520 cubic feet per second

## Slide 32
STREAM | RECURRENCE INTERVAL
Ischua Creek tributary | 4
Allegheny River | 1.25
Ball Creek | < 1
Chadakoin River | 2
Canadaway Creek | 1.5
Silver Creek | > 500
South Branch Cattaraugus Creek | > 500
Cattaraugus Creek at Gowanda | 45
Grannis Brook | > 500
Thatcher Brook | > 500
Buffalo Creek | 1.5
Cayuga Creek | 2
Cazenovia Creek | 40
Tonawanda Creek at Attica | 2.5
Oatka Creek at Warsaw | 2

## Slide 33
Flash Floods of August 10, 2009, in Gowanda and Silver Creek, New York
By Carolyn O. Szabo, USGS, Ithaca
William F. Coon, USGS, Ithaca, (wcoon@usgs.gov) and
Thomas A. Niziol, NWS, Buffalo
Scientific Investigations Report 2010-5259
Available online at USGS Publications Warehouse
Prepared in cooperation with the Federal Emergency Management Agency

## Slide 34
USGS RESPONSE TO FLOODS
FLASH FLOODS of AUGUST 10, 2009
Gowanda and Silver Creek, NY
Cattaraugus Creek
New York State Thruway
Notes: Cattaraugus Creek at NYS thruway