## Slide 1: Heavy Freezing Spray on Lake Michigan 1/1/11
Mike Bardou and Mark Ratzer
National Weather Service
Chicago/Romeoville, IL

## Slide 2: FAM Float
An inside look into the marine environment and forecast impacts
Established a relationship with the Captain
Allowed us to obtain a first-hand account of this event

## Slide 3: Wilfred Sykes: 1/1/11

## Slide 4: Route of the Wilfred Sykes
At least 2” of ice in 90 min
FPTM4
NPDW3

## Slide 5: Captain’s Log…
Waves 12-18 ft on Green Bay
Rapid ice accretion…~ 2” in 90 min
  From Minneapolis Shoal to Porte Des Morts
Spray over the pilothouse with every wave
4-5” of ice accumulation after 6-7 hours

## Slide 6: Why are we doing this?
Rare opportunity to evaluate freezing spray tools thanks to:
  Riveting video
  First-hand accounts thanks to relationships forged from the recent FAM Float

## Slide 7: Forecasting Freezing Spray
Algorithm (Overland 1990)

## Slide 8: Freezing Spray Smart Tool
Utilizes Overland Equation
Will automatically calculate PPR based on forecast data
Averages conditions based on length of the Wx grid (can be any duration)

## Slide 9: Tool Evaluation
Compare GFE Tool to algorithm for this event
  Are the results the same?
  Did the tools indicate heavy freezing spray?
Selected FPTM4 for data because of representative wind observations and reasonable proximity to the route of the Sykes
Evaluate impact of Wx grid length on freezing spray forecast (time averaging of elements)

## Slide 10: Wind and Air Temp at FPTM4:
16Z Fairport, MI: 22032g42kt, Air Temp -3.9 C

## Slide 11: Surface Water Temperature:
Clouds restricted satellite Temp observation over Green Bay

## Slide 12: Ship Observations: January 2nd
Average: 4 C

## Slide 13: Algorithm vs. GFE
Water Temp: 4.0 C
Air Temp: -3.9 C
Wind Speed: 33 KT
Wind Gust: 42 KT
PPR = 39.28
PPR = 38.36 = moderate icing
GFE value of 1 = moderate icing
At 16 UTC
So, Tool agrees with algorithm!

## Slide 14: GFE Smart Tool: Time Averaging
Freezing Spray Forecaster Tool averages over the length of time of a basic weather grid
Weather grids can be from 1 hour, to several days long
Can have negative effects on freezing spray tool output?

## Slide 15: Methodology:
Used hourly wind, gust and air temp data from FPTM4 (12Z-24Z January 1, 2011)
Used lake surface temp of +4 C (averaged from ship obs on Jan 2nd)
Created output for 12, 6, 3 and 1 hour GFE weather grids for comparison

## Slide 16: 1/1/11 FPTM4 Observations:
Notice: increasing winds, decreasing air temp

## Slide 17: 12 Hour Weather Grid:
Freezing spray algorithm output is averaged over entire 12 hour period

## Slide 18: 6 Hour Weather Grids:
Better: captures heavy freezing spray beyond 18Z

## Slide 19: 3 Hour Weather Grids:
Better Still: Ramps up from none/light to moderate then heavy

## Slide 20: 1 Hour Weather Grids:
Best: Depicts more temporal detail, with Heavy Freezing Spray by 17Z

## Slide 21: What Have We Learned?
GFE Freezing Spray Forecaster tool output is time averaged – requires higher temporal resolution to weather grid for best results
Actual conditions observed by boats are often more severe than what buoys or shore-based observing sites may indicate
As always, this tool is just one of many for use in producing a good forecast!

## Slide 22: Questions?